## Slide 1: Motion Priors
Luke Smith
Towards automated MoCaP

## Slide 2: Introduction

## Slide 3: Context
Ultimate goal
  Automated MoCap system
  RGB video -> realistic motion
  No clunky suits

## Slide 4: Current system
Per frame pose predictions
  Issues
    Temporally uncorrelated => jitter
    Trouble with occlusions
  Adopted solution
    Optimise the sequence of poses with smoothness losses
Per-frame prediction
Occlusion issues

## Slide 5: Motion Priors
Motion prior?
  A model that has learnt how humans move
  e.g. through next pose prediction
And then what?
  Constrain a sequence of pose estimations using the prior

## Slide 6: HuMoR Paper
‘Human Motion Model for Robust Estimation’
Paper describes:
  Motion prior model
  Use in improving frame-by-frame pose predictions
Used as a starting point for my project

## Slide 7: HuMoR
1. Motion Prior
Root translation
Root orientation
Body pose (joint angles)
Joint positions
Velocities
Parametrises the small model
Change in state
Model
State
Conditional VAE
Note

## Slide 8: HuMoR
2. Motion optimisation: objective
Objective
Likelihood of latent transitions and initial state
Reprojection to 2d joint predictions
Various regularisers
Given a sequence of 2d pose estimations

## Slide 9: HuMoR
2. Motion optimisation: more concretely
Rollout
What we apply the loss terms on

## Slide 10: HuMoR
2. Motion optimisation

## Slide 11: What I’ve been up to

## Slide 12: HuMoR Evaluation
The good
Smooth motion
Nice occlusions

## Slide 13: HuMoR Evaluation
The bad
Angle representation issues
Not so nice occlusions

## Slide 14: HuMoR Evaluation
The worse
Out of distribution motion…

## Slide 15: HuMoR Evaluation
Comments
Issues
  Unusably slow
      20+mins for 8s video
  Issues with angle representation
  Evaluation didn’t result in a clear yes/no decision
      Improves results in some occluded situations
      Seems worth investigating
Issue 1 is to be addressed first
  Not viable without speedup

## Slide 16: HuMoR Evaluation
Why so slow?
Profiling revealed the ‘rollout’ is the issue
  Rollout is slow
  Rollout results in large computation graph
  Backward step is slow

## Slide 17: HuMoR Improvement
How to speedup
With rollout
Without rollout
Idea of Jakobs’

## Slide 18: HuMoR Improvement
Implementation
I have largely implemented this new method
Currently trying to get it do something useful
  Bug fixing
  Investigating the different losses
  Considering new losses

## Slide 19: What’s next?
Finish the new optimisation method
  Decide if it’s viable
    If so
      Work on improving the motion model
        Relies on SMPL, which we won’t use
        Idea of GNN’s
    If not
      Other ways to use the HuMoR prior?
      More paper reviews?
      Pivot to a new direction?

## Slide 20
Questions/Comments?